## Slide 1
Realization of a mobile virtual loudspeaker setup for the playback of multi-channel audio content
Pranav Sharma, Syed Muhammad Ahmed

## Slide 2
“LOUDSPEAKERS TO GO”
Pranav Sharma, Syed Muhammad Ahmed

## Slide 3: Motivation
Multi-channel speaker require significant physical space
Headphones lacks spatial cues
Use dynamic binaural synthesis system
Create immersive and realistic audio
Greater convenience and accessibility
Revolutionizing Industries like Gaming, Music, Film production

## Slide 4: AIM
Development and Evaluation of a complete system
Portable/partially mobile PC platform
Head and Body sensors required
Head rotation horizontal & vertical directions
Virtual loudspeaker positions remain stationary
Ability to change virtual surrounding
Fig : Head Orientation Change ONLY
Fig : Body Orientation Change ONLY

## Slide 5: Dynamic Binaural Synthesis via Headphones
Create virtual 5-channel 3D sound field for headphones
HRTF-based Binaural Synthesis : KEMAR data set from Aachen
Synthesized BRIRs using SDM
    Accurate capture of sound field in the room
    Realistic reproduction of acoustic characteristics
    Precise sound localization cues for listener
  Saved SDM Rendered RIRs in .mat files, variable for each channel
5 Channel
Audio Content

## Slide 6: PyBinSim
Real Time Binaural processing in python
Using Open Sound Control (OSC) protocol
Powerful tool for creating immersive binaural Audio Experience
Track listener/source position and orientation
Tools for reading RIRs, manipulating and processing
Use this tool as spatializer for this project
Fig: Yaw, Pitch and Roll

## Slide 7: Open Sound Control (OSC)
Protocol for exchanging messages in multimedia applications
Send and receive OSC messages in Python
Message includes string identifier for desired filter
Maps OSC addresses to functions
Updates ds_filters, early_filters, late_filters
Fig: OSC flow diagram

## Slide 8: System Architecture
Divided in two parts
    Controller
    Processor
  Controller acts remote to control PyBinSim
  Processor controls signal flow
  OSC acts as request handler

## Slide 9: PyBinSim Processor
Central hub for binaural audio rendering
Utilizes OSC library for real-time control
Parse and load discrete filters for synthesized BRIRs
Real time convolution and sound buffering based on pose values
Fig: PyBinSim controller flow

## Slide 10: PyBinSim Controller
Remote Control to pyBinSim
Handles sensor data, sends updates via OSC
Uses Tkinter for a simple, interactive User Interface
Button presses trigger OSC messages to processor

## Slide 11: Sensor Data Handling
Head sensor (Bridgehead tracker)
Body Sensor (RealSense t265)
Fast sensor inputs from head and body handled
Body pose data acts as an offset for head tracking data
Calculated offsets are transmitted to the pyBinSim processor
Fig: Reasense T265
Fig: Bridgehead tracker

## Slide 12: User Interface
Audio adjustments, orientation resets, tracking
Button-specific functions, OSC messages
Used Multiprocessing
    Run UI and PyBinSim together
    Close both together

## Slide 13: Experimental Setup
Developed in Listening lab
Attached body tracker with backpack
Block size (1024),Processing power trade-off
Room database used in project
    Listening Lab (HL): RT 0.255s
    Editorial Room Media Lab 2 (ML2-102): RT 0.52s
    Seminar Room (H2505): RT 1,2s
    Audio/Video Lab (H1593b): RT 0.28s
  Divided into stages (Standing, Head motion, Overall motion)

## Slide 14: Results
5 Subjects participated
Everyone could feel room change
Sound coming within the room
Good stability and Localization of sources
  Good experience rating
Notes: Stage Question Type Percentage scores Mean values
------------------------------------------------------------------------------------------------------------------------------------------------------------------------
Stage 1 Question 2 (1-5) Quality 84 4.2
Question 3 (1-5) Localization 92 4.6
-----------------------------------------------------------------------------------------------------------------------------------------------------------------------
Stage 2 Question 4 (1-5) Stability 88 4.4
Question 5 (1-5) Latency 84 4.2
Question 6 (1-5) Localization individual sound 92 4.6
Question 7 Externalization Outside the head Outside the head
-----------------------------------------------------------------------------------------------------------------------------------------------------------------------
Stage 3 Question 8 (1-5) Stability 88 4.4
Question 9 (1-5) Latency 76 3.8
Question 10 (1-5) System move with you 84 4.2
Question 11 (1-5) Localization 88 4.4
Question 12 (a,b and c) Externalization Outside the head Outside the head
Question 13 (1-5) Overall Experience 92 4.6
----------------------------------------------------------------------------------------------------------------------------------------------------------------------------

## Slide 15: Discussion and Outlook
Successfully Developed a dynamic binaural synthesis system
Enhanced user interface for interactive sound control and visualization
Real-time tracking of head and body movements
Potential improvements
    Sensor optimization
    Wireless capability
    Integration of smaller, wearable sensors

## Slide 16: Future Scope
There is scope for further research
Spatial Cognition and Localization
Virtual room environments' influence on sound perception
Personalized HRTFs
Auditory Scene Analysis
Integration with Visual Stimuli

## Slide 17: Summary
Headphones not reproduce spatial cues, Binaural Synthesis plausible solution
SDM rendered BRIRs for spatial accuracy
Our project divided in PyBinSim controller and processor
Validated the system to go application
Good localization and envelopment, bit latency issues, overall good ratings
System can be optimized and used for further research purposes

## Slide 18: QnA